Annex No. 1 – Technical specifications

Technical specifications

Set of student workstations for testing ADAS systems

- The subject of the public contract is the supply of 3 sets of student workstations for testing ADAS systems for educational purposes. The intention is to acquire smaller and simpler HIL test devices for validating ADAS systems in automotive. The device should be able to stimulate the analog and digital inputs of the tested control unit, while monitoring its outputs. The test equipment must contain test and simulation HW.

1 piece/set includes:

  - cabinet / box for placement on the table;

  - real-time simulation module;

  - analog and digital I/O module/s;

  - additional cabling.

The subject of performance also includes transport to the place of performance.

Manufacturer of the device:				to be completed by the participant

Exact type designation of the device:		to be completed by the participant

Number of sets:					3

Set of student workstations for testing ADAS systems must meet following criterias:

| Basic technical parameters | Minimal required values – obligatory condition! | Value of the offered device |
| --- | --- | --- |
| a) cabinet / box for placement on the table |
| Modular solution | Yes | the participiant indicates YES/NO |
| Number of slots / modules | min. 6 | the participiant indicates YES/NO and indicates specific value |
| Power voltage: 12 VDC / 230 VAC | Yes | the participiant indicates YES/NO |
| "On the table" design | Yes | the participiant indicates YES/NO |
| b) Real-time simulation module |
| Real-Time CPU unit | Yes, min. 2,7 GHz | the participiant indicates YES/NO and indicates specific value |
| The number of CPU cores of the unit | min. 6 | the participiant indicates YES/NO and indicates specific value |
| RAM memory | min. 32 GB | the participiant indicates YES/NO and indicates specific value |
| PCI Express interface | Min. 4 | the participiant indicates YES/NO and indicates specific value |
| Ethernet interface | Yes, 1 Gbit/s | the participiant indicates YES/NO and indicates specific value |
| Active CPU cooling | Yes | the participiant indicates YES/NO |
| USB interface | Yes, USB 3.0 | the participiant indicates YES/NO and indicates specific value |
| SSD drive | Yes, min. 64 GB | the participiant indicates YES/NO and indicates specific value |
| Installation in a cabinet a) | Yes | the participiant indicates YES/NO |
| c) Analog and digital I/O module/s |
| Output analog voltage | min. 0 ÷ 40 V | the participiant indicates YES/NO and indicates specific value |
| Output analog current | 100 mA | the participiant indicates YES/NO and indicates specific value |
| Number of analog channels | min. 4 | the participiant indicates YES/NO and indicates specific value |
| Internal resistance decade range | 10 ÷ 10000 Ω | the participiant indicates YES/NO and indicates specific value |
| PWM generation range | 0,2 ÷ 25000 Hz | the participiant indicates YES/NO and indicates specific value |
| Measurement of output quantities | Yes | the participiant indicates YES/NO |
| Measurement value available in the simulation SW | Yes | the participiant indicates YES/NO |
| Input digital voltage | min. -40 ÷ +40 V | the participiant indicates YES/NO and indicates specific value |
| Input digital stream | 0 ÷ 800 mA | the participiant indicates YES/NO and indicates specific value |
| PWM measurement range | 0,2 ÷ 200000 Hz | the participiant indicates YES/NO and indicates specific value |
| Output digital voltage | 0 ÷ 25 V | the participiant indicates YES/NO and indicates specific value |
| Output digital stream | 0 ÷ 30 mA | the participiant indicates YES/NO and indicates specific value |
| Number of digital channels | min. 16 | the participiant indicates YES/NO and indicates specific value |
| Adjustable threshold for sampling the input sig. | Yes | the participiant indicates YES/NO |
| Sampling interval | 50 µs | the participiant indicates YES/NO and indicates specific value |
| d) Additional cabling |
| Termination resistors for the CAN bus | min. 30 | the participiant indicates YES/NO and indicates specific value |
| Cable for connecting the OBDII socket and CAN | min. 1 | the participiant indicates YES/NO and indicates specific value |
| Y fork for CAN | min. 4 | the participiant indicates YES/NO and indicates specific value |
| Gender changer male/male for 9-pin d-Sub | min. 8 | the participiant indicates YES/NO and indicates specific value |
| Gender changer female/female for 9-pin d-Sub | min. 4 | the participiant indicates YES/NO and indicates specific value |

The participiant should enter the data in compliance with the technical specification of the offered devices.